## Slide 1: Current status of Information Technology in DPCP
Piotr Kotecki
Du Pont Conoco Poland
Notes: 1

## Slide 2: Du Pont Conoco in Poland
86 employees (51 in Conoco) + 2 permanent cooperators (in Elastomers SBU)
HQ in Warsaw (62 persons)
Compu-Touch LAB in Warsaw (3 persons)
Office of Fibbers SBU in Lodz (4 persons)
17 regional representatives

## Slide 3
Workstations
Dell Pentium 75,100,133 or 166 with 16/32MB RAM or Dell 486
MS DOS 5.0 or MS DOS 6.2
NIC - mainly 3COM
WIN 3.1, MS Office 4.2
Portables
Dell Latitude 486/75MHz or P5/75,100,133 or 150MHz
16/24/32 MB RAM; MS DOS 6.2
NIC in Docking Stations: SMC900 or 3COM
WIN 3.1, MS Office 4.2
Printers
8 Network printers: HP Laser Jet III,IIID,4M/MV, 5N, 5M
HP LJ IIP connected to PAD
Telex Gateway with telex modem
Gateway for E-Mail with US Robotics Courier modem
Novell NetWare Server
HP LF 4/66 (486/66 MHz)
72 MB RAM
Hard disks - SCSI: 5 x 2GB (8GB in Raid 5) 1 x 200MB
Backup streamer
HP SureStore 12000
Backup software Arcserve
LAN - Ethernet
NetWare 3.12 for 100 users
(we use up to 75 entries)
DPCP - HQ in Warsaw
4 x 24 ports HUBs (Cabletron SEHI-24 + 3*SEH-24 10BaseT)
14 port free
IT Infrastructure of DPCP HQ office in Warsaw
Modems
Boca, US Robotics, MultiTech
connection with City and ING banks
intranet
stations
IPX/SPX protocol
MS Windows NT 4.0 server
Dell Power Edge 4100
128 MB RAM
HDD SCSI: 3*4GB (8GB in Raid 5) Backup streamer: Dell
US Robotics Courier modem
Petrol stations (Compu-Touch)
168 of outlets in the office
~90 of free outlets
27 of remote Ms Mail users
PAD X.25
Leased modem from Polpak
leased X.25 line 9.6kb
MS Windows NT 4.0 workstation
Dell GXi P5166/64MB
2 GB HDD IDE
NT
IPX/SPX protocol
Macintosh Quadra 650
modem
printer DataProduct LZR 1580
AG Paris
Notes: 1

## Slide 4
Connections of DPCP HQ with outside world
Warsaw office
Petrol stations
leased line 9.6kb/s ( X.25) 8 channels
dial-up connection
Geneva
HP PAD up to 12 users
Ms Maill HUB in
UK (Warwick)
Intranet,
Internet
4 stand alone PCs for
connection with stations
2 PCs for Intranet and Internet
connection
1 stand alone PC for
Ms Mail connection
1 stand alone Mac for
connection with AG Paris
2 PCs for connection with City&ING Banks
1 stand alone PC Telex Gateway
banks
AG Paris
Publics network
telex connection